Tower
Purpose: Serve as Herbert’s room (interior) and the French Taunter perch (exterior)
Components: Hexagon, 3 walls, 5-6 ladder slats
Size: Roughly 7’ x 7’ x 12’
Considerations: Strong, easily movable, exterior and interior, access to top through interior, large window in wall
Construction:
- Install side structure in one divot, as well as side and top structure in the other divot
- Clad side of one divot, floor top and clad side of other
- Install ladder slats between support poles for top access through remaining hole
- Place additional flooring inside hexagon if necessary
- Fabricate three 4’ by 6’ walls, one with a large arched window
- Clad exterior side of each wall, lift into place atop hexagon, and install
- Clad interior side of walls, paint, and add details to interior